## Slide 1: A brief Introduction to Particle Filters

## Slide 2: Many different names…
(Sequential) Monte Carlo filters
Bootstrap filters
Condensation
Interacting Particle Approximations
Survival of the fittest
…
Particle Filters

## Slide 3: Sample-based PDF Representation
Monte Carlo characterization of pdf:
  Represent posterior density by a set of random i.i.d. samples (particles) from the pdf p(x0:t|z1:t)
  For larger number N of particles equivalent to functional description of pdf
  For N approaches optimal Bayesian estimate

## Slide 4: Sample-based PDF Representation
Regions of high density
  Many particles
  Large weight of particles
Uneven partitioning
Discrete approximation for continuous pdf

## Slide 5: Importance Sampling
Draw N samples x0:t(i) from Importance sampling distribution (x0:t|z1:t)
Importance weight
Estimation of arbitrary functions ft:
Notes: Usually impossible to draw efficiently from p  importancr sampling

## Slide 6: Sequential Importance Sampling (SIS)
Augmenting the samples
Weight update
Notes: factoring importance density
Markov assumption; not necessary to keep all former states in memory

## Slide 7: Degeneracy Problem
After a few iterations, all but one particle will have negligible weight
Measure for degeneracy: Effective sample size
Small Neff indicates severe degeneracy
Brute force solution: Use very large N
wt* ... true weights at time t
Notes: Updating these particles means a lot of computational effort, for particles whose contribution to the approximation of p(x|t) is almost zero

## Slide 8: Choosing Importance Density
Choose  to minimize variance of weights
Optimal solution:
Practical solution
  importance density = prior
Notes: drawbacks of optimal solution: sampling from complicated distribution, evaluation of integral over new state for weight estimation
restricted cases where optimal case is possible: finite state set,Gaussian transition model

## Slide 9: Resampling
Eliminate particles with small importance weights
Concentrate on particles with large weights
Sample N times with replacement from the set of particles xt(i) according to importance weights wt(i)
„Survival of the fittest“
Notes: resample whenever effective sample size falls below certain threshold
resulting particles have uniform weight

## Slide 10: Sampling Importance Resample Filter: Basic Algorithm
1. INIT, t=0
  for i=1,..., N: sample x0(i)~p(x0); t:=1;
2. IMPORTANCE SAMPLING
  for i=1,..., N: sample xt(i) ~ p(xt|xt-1(i))
    x0:t(i) := (x0:t-1(i), xt(i))
  for i=1,..., N: evaluate importance weights wt(i)=p(zt|xt(i))
  Normalize the importance weights
3. SELECTION / RESAMPLING
  resample with replacement N particles x0:t(i) according to the importance weights
  Set t:=t+1 and go to step 2

## Slide 11: Variations
Auxiliary Particle Filter:
  resample at time t-1 with one-step lookahead (re-evaluate with new sensory information)
Regularisation:
  resample from continuous approximation of posterior p(xt|z1:t)

## Slide 12: Visualization of Particle Filter
unweighted measure
compute importance weights  p(xt-1|z1:t-1)
resampling
move particles
predict p(xt|z1:t-1)

## Slide 13: Particle Filter Demo 1
moving Gaussian + uniform, N=100 particles

## Slide 14: Particle Filter Demo 2
moving Gaussian + uniform, N=1000 particles

## Slide 15: Particle Filter Demo 3
moving (sharp) Gaussian + uniform, N=100 particles

## Slide 16: Particle Filter Demo 4
moving (sharp) Gaussian + uniform, N=1000 particles

## Slide 17: Particle Filter Demo 5
mixture of two Gaussians,
filter loses track of smaller and less pronounced peaks

## Slide 18: Obtaining state estimates from particles
Any estimate of a function f(xt) can be calculated by discrete PDF-approximation
Mean:
MAP-estimate: particle with largest weight
Robust mean: mean within window around MAP-estimate

## Slide 19: Pros and Cons of Particle Filters
Estimation of full PDFs
Non-Gaussian distributions
  e.g. multi-modal
Non-linear state and observation model
Parallelizable
Degeneracy problem
High number of particles needed
Computationally expensive
Linear-Gaussian assumption is often sufficient

## Slide 20: Agenda
Problem Statement
Classical Approaches
Particle Filters
Theory
Algorithms
Applications

## Slide 21: Mobile Robot Localization
Animation by Sebastian Thrun, Stanford
http://robots.stanford.edu

## Slide 22: Positioning Systems1
1: Gustafsson, et.al.: Particle Filters for Positioning, Navigation and Tracking. IEEE Transactions on Signal Processing Vol. 50, 2002
Track car position in given road map
Track car position from radio frequency measurements
Track aircraft position from estimated terrain elevation
Collision Avoidance (Prediction)
Replacement for GPS

## Slide 23: Model Estimation
Tracking with multiple motion-models
  Discrete hidden variable indicates active model (manoever)
Recovery of signal from noisy measurements
  even if signal may be absent (e.g. synaptic currents)
  mixture model of several hypotheses
Neural Network model selection [de Freitas]1
  estimate parameters and architecture of RBF network from input-output pairs
  on-line classification (time-varying classes)
1: de Freitas, et.al.: Sequential Monte Carlo Methods for Neural Networks. in: Doucet, et.al.: Sequential Monte Carlo Methods in Practice, Springer Verlag, 2001

## Slide 24: Other Applications
Visual Tracking
e.g. human motion (body parts)
Prediction of (financial) time series
e.g. mapping gold price  stock price
Quality control in semiconductor industry
Military applications
Target recognition from single or multiple images
Guidance of missiles

## Slide 25: Possible Uses for our Group
Reinforcement Learning
  POMDPs
  Estimating Opponent States
RoboCup: Multi-robot localization and tracking
Representation of PDFs
Prediction Tasks
Preprocessing of Visual Input
Identifying Neural Network Layouts or other Hidden System Parameters
Applications in Computational Neuroscience (?)
Other suggestions?

## Slide 26: References
Doucet, de Freitas, Gordon: Sequential Monte Carlo Methods in Practice, Springer Verlag, 2001
Arulampalam, Maskell, Gordon, Clapp: A Tutorial on Particle Filters for on-line Non-linear / Non-Gaussian Bayesian Tracking, IEEE Transactions on Signal Processing, Vol. 50, 2002

## Slide 27
Thank you!